## Slide 1: ISVMA Master Class
Radiology

## Slide 2: Kimberly King CVT
A little about me
  Bachelors of Science: Biology
  Associate of Veterinary Technology
  CVT for 7 years
  GP for 14 years
  Current position: Lead Tech Veterinary Diagnostic Centers
  Passed the VTNE in 2019

## Slide 3: What scares you about VTNE?
Radiology Questions (lets really use that chat feature here)
BE HONEST!!! ITS SCARY!!!
Remember the basics. They do not change.
Keep it simple. If you remember the basic principles the rest will follow

## Slide 4: AGENDA
Understand radiation safety
Master image production basics
Recognize common positioning & artifacts
Prepare for VTNE-style questions

## Slide 5: Safety First, as it should be
ALARA principle
Distance, time, & shielding
Inverse square law
Occupational dose limits
Who can restrain patients
PPE: lead apron, gloves, thyroid shield, eye protection

## Slide 6: ALARA principle
As Low As Reasonably Achievable
Protect yourself and your patient
Always use a collimator and use the smallest possible aperture that will cover the anatomic area of interest
Never permit any part of your body to be in the path of the primary x-ray beam
Positioning is key
Premedication for patient (hands free radiology)

## Slide 7: Distance, Time, Shielding
Distance: Maximize the distance from the radiation source, as intensity decreases with distance.
Time: Minimize the duration of exposure to reduce total dosage.
Shielding: Use appropriate barriers (e.g., lead aprons, concrete walls) to block or absorb radiation.

## Slide 8: Inverse square law
Radiation intensity decreases the farther you get away from it.
Doubling distance= ¼ exposure
Stand as far away as possible

## Slide 9: Occupational dose limits
Legal Records (hint)
  What needs to be displayed on a radiograph?
  Name, Date, Signalment, Clinic information
Radiation exposure is cumulative
  Dosimeter badges are required
  Report sent to you quarterly
  Bring your totals with you between jobs

## Slide 10: Occupational dose limits
It's okay to say NO…..
  If you are on your 9th radiograph of the day and need to switch out its okay.
  Remember this is the WRONG type of GLOWING
Advocate for yourself and for your patients

## Slide 11: Restrain Patients
Who can restrain patients
  Only those who have been trained should be restraining
Must always where the correct size of PPE
Never hold the tube (dental) or cassette (xray table) in place.
  If its broken get it fixed and in the meantime DO NOT USE IT.
Pregnancy precautions
  Should avoid exposure
When able never manually restrain if sedation is possible (Hands Free Radiology)

## Slide 12: Personal Protective Equipment (PPE)
PPE MUST BE at least 0.5mm lead equivalent
Apron / Vest & Skirt: Protects the chest, abdomen, and pelvis from scatter radiation.
Thyroid Shield / Collar: Wraps around the neck to protect the thyroid gland, very sensitive to radiation.
Lead Gloves: Barrier for the hands during procedures where hands may be in close proximity to the beam.
Lead Glasses: Protects the lenses of the eyes from scatter exposure.
Eye Protection: Most sensitive part of the body to radiation exposure.

## Slide 13: What is missing from this picture??
Where is the thyroid guard?
Where is the eye protection?
Where are the gloves?
Where are their dosimeter badges?

## Slide 14: Keep your equipment in the best condition
Check it regularly
  Any cracks or wear replace immediately
Don’t drop them on the table or floor
  Always hang them up
If its broken do not use it

## Slide 15: Hands Free Radiology (real life exposure)
Reduce time, Increase distance, and minimize radiation exposure
Great resource VETgirl (Great poster with guidelines)
What every practice should be striving for the safety of the staff and their patience
Its not just a diagnostic tool, it’s a procedure. Treat it as such.
Premedication, sedation as needed

## Slide 16: 1st radiology VTNE question
True or False: Sedated animals can be manually restrained.
Answer: True
Sedation level does not affect manually restrain.

## Slide 17: Which PPE is required when personnel must be in the radiography room?
A. Lead apron only
B. Lead gloves only
C. Thyroid shield only
D. Lead apron, gloves, and thyroid shield
Answer: D

## Slide 18: Let's produce the best radiograph
KVP vs mAs a VTNE favorite

## Slide 19: KVP (beam energy)
Kilovolt Peak
X-rays penetrate tissue more easily
More photons reach the detector
What happens when you increase kVP?
  Image becomes darker (more exposure)
  Quality of image not as good
  Image looks less black and white
Higher kvp for thicker or dense body parts (abd, pelvis)
Lower kvp for tinner parts (limbs, digits)

## Slide 20: mAs (beam quantity)
Milliampere-seconds
The number of X-ray photons produced
mAs= mA x exposure time
What happens when you increase mAs
More photons are produced
Image becomes darker
Contrast stays roughly the same
Patient dose increases proportionally

## Slide 21: Easy Comparison Guide
Factor | kVp | mAs
Controls | Beam energy | Beam quantity
Affects penetration? | Yes | No
Affects contrast? | Yes (higher kVp = lower contrast) | Minimal
Affects image darkness? | Yes | Yes
Affects patient dose? | Yes | Yes (directly proportional)

## Slide 22: 15% rule
The 15% rule describes the relationship between kVp and image receptor exposure.
Increasing the kVp by 15% (doubles image receptor exposure)
Decreasing the kVp by 15% (halves image receptor exposure)
Compensate with mAs
(Increase your kVp, Decrease you mAs)
(Decrease you kVp, Increase you mAs)

## Slide 23: How do we make this radiograph better?
Effects of underexposure
mAs too low
kVP too low

## Slide 24: How do we make this radiograph better?
Effects of overexposure
mAs too high
kVP too high

## Slide 25: VTNE QUESTION (a form of this question will be on the test)
Which setting control image density?
kVP
mAs
Collimation
Grid
Answer: B

## Slide 26: Positioning Essentials
Positioning is key for the best image and for limiting exposure
Collimating a radiograph properly
Having the proper positioning tools will help produce the best pictures

## Slide 27: Thorax views
3 views
  Right lateral
  Left lateral
  VD or DV (when should you use the DV view?)
Thoracic radiographs taken on inspiration
  How does air look on radiograph?
Thorax landmarking
  Caudal scapula

## Slide 28: Abdominal Views
3 views
  Right lateral
  Left lateral
  VD
Abdominal radiogrpahs taken on expiration
Abdomen landmarks
  Last rib

## Slide 29: Whole Body Radiographs
Don’t do them.
  You will lose the fine detail
Collimation is key
Use the tools in your tool box, to get the best answers

## Slide 30: Pelvic views
Hip dysplasia positioning
  Ventrodorsal view
  Hind limbs extended
  Femurs parallel
  Pelvis straight
Landmarking basics
  Joints: joint space

## Slide 31: Pelvic Views

## Slide 32: Orthopedic Limb Images
Centering your pointing of interest
Collimating is key
Compare both limbs when able

## Slide 33: What's wrong with this image??
It is to far out.
What else is in that image?
There is only one limb for comparison.

## Slide 34: Dental Radiology
All the same basics apply, just on a much smaller scale.
Positioning is key
Enlongating vs shorting
Practice is key

## Slide 35: Dental Radiograph Importances
Dental disease is often below the gumline
Periodontal disease stages
Tooth root abscesses
Resorptive lesions

## Slide 36: Elongating vs Shortening Dental Radiographs
Elongating
Caused by the x-ray head being too parallel
Shortening
Caused by the x-ray head being too perpendicular

## Slide 37: 60, 45, 90 repeat
Postion is key to any dental radiograph
Once you get that tooth on image you can always adjust your kvp or mAs to get the image you need

## Slide 38: Bad Practices
Take your hands out of the radiographs
Safety first
  Should be wearing all the same PPE
Hands Free Radiology skills still apply

## Slide 39: Break it down..hehe
Back in 5 minutes

## Slide 40: Key problems
Motion artifact
Improper collimation
Light vs dark images
Common artifacts (motion, grid lines, debris)

## Slide 41: Motion Artifact
Burly image
Sedation
Hands free radiology

## Slide 42: Improper Collimation
Loss of detail
Loss of correlation
Grid lines

## Slide 43: Image to dark vs light
Most machines will adjust based on weight.
Body habitus, Fluid, etc.
Remember your Kvp or Mas if needed to adjust

## Slide 44: Artifacts in image
What is the metal line??
Superimposed object or a concern
Hands in the radiograph

## Slide 45: Contrast Studies
Barium vs iodinated contrast
When barium is contraindicated
Cystograms
Myelograms
Double-contrast studies

## Slide 46: Barium vs Iodine
Barium
  GI studies
  Contraindicate with perforation
Iodine
  Safer if rupture suspected
  Used for urinary and spinal studies

## Slide 47: Other forms of Digital Imaging
Ultrasound
CT
MRI

## Slide 48: Ultrasound
My new favorite diagnostic tool
Sound waves
Echocardiograms and Abdominal ultrasounds
Fine detail on organs
No sedation required

## Slide 49: CT
Computed Tomography
cross-section (“slice”) images of your pet’s body
CT scan = best for structure (bones, lungs, tumors)
Very fast (seconds to minutes) compared to MRI
Sedation Required

## Slide 50: MRI
Magnetic Resonance Imaging
MRI = best for soft tissue (brain, nerves)
powerful magnets and radio waves (not X-rays)
MRI scans can take 30–90 minutes
Sedation Required

## Slide 51: Lets put our knowledge to the test…just for fun
8 possible VTNE questions.
All multiple choice
Remember this is just for fun to see watch knowledge you have retained.
Let’s talk test anxiety

## Slide 52: Increasing mAs will result in:
A. Decreased image density
B. Increased image density
C. Increased contrast
D. Decreased distortion
Answer: B

## Slide 53: Which factor has the greatest effect on radiographic contrast?
A. mA
B. Exposure time
C. kVp
D. SID
Answer: C
Kvp VS MaS WILL BE ON THE TEST IN SOME FASHION.

## Slide 54: The primary purpose of collimation during radiography is to:
A. Increase image density
B. Reduce scatter radiation
C. Shorten exposure time
D. Increase contrast resolution
Answer: B

## Slide 55: Which imaging technique uses sound waves?
A. X-ray
B. CT
C. MRI
D. Ultrasound
Answer: D

## Slide 56: Which of the following is the most effective way to reduce radiation exposure?
A. Increase exposure time B. Stand closer to the beam C. Use proper shielding D. Hold the patient manually
Answer: C

## Slide 57: A radiograph appears too light. What is the most likely cause?
A. Overexposure B. Excessive kVp C. Underexposure D. Too much scatter
Answer: C

## Slide 58: Which structure is best evaluated on a right lateral thoracic view?
A. Left lung inflation B. Cardiac silhouette only C. Sternum D. Pelvis
Answer: A

## Slide 59: Which term describes sharpness of an image?
A. Contrast B. Density C. Detail D. Distortion
Answer: C

## Slide 60: Key Takeaways
Safety first, always
Know kVp and mAs
Proper positioning is critical
Artifacts are common VTNE questions
Digital doesn’t always mean safer exposure

## Slide 61: Resources for more information
IDEXX positioning guides (free PDFs)
  https://www.idexx.com/files/radiography-positioning-guide.pdf
VIN (Veterinary Information Network)
Veterinary Oral Health Council
https://vohc.org/

## Slide 62: Thank you again
If you have additional questions. Please reach out.
www.linkedin.com/in/kimberly-king-589485b9
Any questions?